1. Preface
  1. Reserach group description
2. Introduction
  1. Introduction to HEVs
  2. Energy Management Systems
  3. Project objectives for Summer Internship
    1. C port existing DP-PMP power management system
    2. Develop own DP algorithm optimizing fuel use
      1. Based on three state variables: discretized battery energy level, integer engine on-off control, and discrete gear state.
    3. Control theory – tie in to EE
3. Problem Description
  1. Vehicle Model
    1. Working with a priori New European Driving Cycle (NEDC) speed and slope profile data.
    2. Longitudinal vehicle dynamics model at wheel
    3. Powertrain model
    4. Power split optimization.
  2. Optimization Strategy Explanations
  3. Problem Formulation
4. Solutions to Problem Description
  1. Original Stephans DP-PMP model
    1. Port to C in order to lower computation demand for implementing management system into a rapid control protyping device.
  2. Dynamic Programming
    1. Finding optimal power split control of an HEV
      Developing Optimal Power Split Controls in Hybrid-Electric Vehicles through
Dynamic Programming Optimization
Electronics Project Internship Report
Asgard Kaleb Marroquin
Technische Universität Dresden, Germany
Summer 2016

Acknowledgements
I would like to especially thank Stephan Uebel, Robert Kloss, Conny Tempelhahn, and Prof. Dr.-Ing. Bernard Baeker for the opportunity to work on such a fascinating subject this summer. Their mentoring, supervision, and advice was instrumental in understanding and developing optimal control theory this summer. I also thank all those at the Innovationzentrum Fahrzeugmechatronik, whose openness and inclusiveness helped me integrate into the mechatronics team professionally, academically, and culturally.
Preface
My internship this summer took place in Dresden, a small city on the east side of Germany, where industry and STEM-related technical training have taken strong root. In particular, I interned with the Innovationzentrum Fahrzeugmechatronik, or the Department of Vehicle Mechatronics, at the Technische Universität Dresden. The department works directly with the transportation agency in Dresden – the Dresdener Verkehrsbetriebe (DVB) – in reducing fuel consumption and heat losses in the city's ever-growing hybrid-electric bus fleet. The group also collaborates with private companies such as Bosch, BMW, and Continentale (CHECK NAMES). The department investigates various vehicle fields, such as power optimization strategies for powertrain management, thermal losses as a result of passenger exchange and a smaller combustion engine size, bus log data analysis, battery technologies, real-time component diagnostics, and conductor assistant systems for more efficient driving cycles.
Introduction
WRITE INTRODUCTION TO HEVS – necessary?
Various control methods have been investigated for optimizing energy management systems, or EMSs, for HEV powertrains. Two main control strategies exist for developing optimal HEV powersplit strategies: numerical methods for known a priori speed trajectories demand profiles (noncausal) and analytical methods without such knowledge (causal) (Jager, Keulen et al 2013, Elbert 2013). Noncausal methods, requiring perfect future driving condition predictions, are able to compute across the entire given driving profile and find globally optimal solutions for EMSs (Tempelhahn, Conny 2016). Were noncausal optimization methods be used in realtime, stochastic inputs deviating from the defined driving cycle would influence calculations; as a result, such methods are typically performed offline and are used as benchmarks for comparing and designing efficient online causal EMSs (Tempelhahn, Conny 2016). Causal methods performing online, on the other hand, can only optimize locally portions of the driving cycle problem and thus return suboptimal strategies (Tempelhahn, Conny 2016).
Dynamic programming (DP) is typically used for calculating globally optimal EMS solutions due to its flexibility and ability to ensure global optimality. DP can utilize both mixed-integer and continuous state variables with nonlinear and nonconvex models, conditions which other methods cannot numerically make function (Elbert 2013, Murgovski, Nikolce et al 2013). However, dynamic programming can only practically optimize an EMS with a limited number of state variables because computational time increases exponentially as more state permutations for a given driving profile are analyzed – i.e. the “curse of dimensionality” (R. Bellman, Dynamic Programming, Princeton, NJ. USA: Princeton Univ. Press, Jun. 1957). DP also requires predetermined travel profile data and is thus noncausal by nature. Nevertheless, due to the repetitive, predictable nature of city bus routes, speed profiles for hybrid-electric transit can be approximated based on past logged data records. Standard driving trajectories, such as the New European Driving Cycle, attempt to mimic urban driving speed profiles and are typically used for determining typical urban emissions (INSERT REFERENCE); these trajectories can also be used as a baseline for testing DP algorithms.
Alternative causal optimization methods such as convex optimization and methods utilizing Pontryagin's maximum principle (PMP) are also thoroughly researched in order to implement online control systems in HEVs. Although far faster than DP, such methods naturally have their limitations. For example, convex optimization requires a linear convex model utilizing continuous state variables in order to function effectively. Should a problem be originally nonconvex, it must be manually made convex, possibly affecting optimality results (Tempelhahn, Conny 2016). And although mixed-integer boolean state variables – engine on-off control, for example – can be theoretically relaxed to become a continuous value between zero and one (Murgovski, Nikolce et al 2013), it was agreed upon by the research group that smoothing out strict boolean controls may yield questionable results at best and the proceudure may not yet be generally accepted as sound. PMP-based strategies are also limited to processing only continuous state variables, but can also find near-globally optimal results for such variables (Tempelhahn, Conny 2016).
Due to the strengths and weaknesses of various different optimization control methods, they are usually combined to exploit each other's characteristics. Faster procedures such as convex optimization and PMP can be integrated into DP algorithms and optimize the continuous variables in the model. This frees up the number of states DP must calculate and dedicates the algorithm to optimize just mixed-integer states, considerably reducing computation time as a result (Uebel, Stefan et al 2016, Murgovski, Nikolce et al 2013). Should a DP-PMP combined method become fast enough on either a predictable hybrid-electric bus route profile or a model European driving cycle,
Two main projects were defined for this summer internship. The first involves further speeding up and converting a DP-PMP algorithm developed by my supervisor so that it may be tested in a Autobox, a rapid control prototyping device. This algorithm, which uses vehicle kinetic energy, battery electric energy, gear selection, and travel time as state variables, minimizes fuel use for an articulated bus model resolved spatially. The details of this control methods can be found in (Uebel, Stefan et al 2016). This project will be briefly described in this report, as it did play a key role in better understanding dynamic programming. The second project, more relevant to working with controls and thus described here in more detail, involved developing a new DP algorithm which would find the optimal power split control of a Ford Focus-like HEV model that could handle a continuous battery energy level state, a discrete gear state, and a boolean engine on-off state. The temporally resolved model, requiring a predefined driving profile, is based on the New European Driving Cycle. By creating a dynamic programming model based on modern control theory which models and optimizes battery use in a hybrid-electric bus at a macroscopic level, this internship has taught me the principles of controls, a fundamental field of electrical engineering.

Problem Description
New European Driving Cycle
The New European Driving Cycle (NEDC), a speed profile mimicking a typical commute in a European urban environment, is used as a vehicular travel profile for the DP algorithm. The driving cycle consists of four Urban Driving Cycle (UDC) periods of driving simulating sporadic low vehicle speed and engine load experienced in cities, followed by an Extra Urban Driving Cycle (EUDC) simulating faster, more aggressive travel (United Nations Environment Programme).

Longitudinal Vehicle Model
In order to optimize the power split control in the HEV, a vehicle model defining a wheel torque demand which will satisfy the NEDC must be defined. To do so, the crankshaft speed and the sum of forces at the wheel must first be determined. The vehicle's velocity vector v, wheel constant rolling radius r, and gear ratio γ(g) define the crankshaft's rotational velocity ω(v,g) (1), where v is the NEDC speed profile discretized every second.
%omega(bold v,g) = bold v over r%gamma(g) (1)
The forces at the wheel can be described though Newton's Second Law (2),
m {d bold v } over {dt} + bold c_%alpha + bold c_%beta + c_a bold v^2 + F_B = (bold F_WHEEL)%gamma(g) (2)
where m is the vehicle mass, dv/dt is vehicular acceleration, cα = m*g*sin(Θgradient) is the vehicle's gradient force, cβ = μdrag*m*g*cos(Θgradient) is the vehicle drag force, Θgradient is the speed trajectory's slope profile (here assumed to be flat). FB are braking forces, and FWHEEL is the amount of force the wheel must deliver. From this, the wheel torque demand TWHEEL = FWHEEL*r for the NEDC can be found. With the wheel torque and crankshaft speed calculated, the crankshaft torque TCRS (3), which must be satisfied by the power drivetrain split during DP calculations, is finally found.
m {d bold v } over {dt} + bold c_%alpha + bold c_%beta + c_a bold v^2 + F_B = (bold F_WHEEL)%gamma(g)

 Parallel drivetrain The project optimizes

References
Elbert (2013)
United Nations Environment Programme