Figure 2: Model parallel HEV drivetrain used. The three state variables (shown as circles) affect how the ICE and EM satisfy the power demanded by the wheels. Dynamic programming analyses state variables possible values and, by controlling their state dynamics at discrete points of time along the NEDC, cumulative fuel use (shown as a triangle) is optimized. Figure based on (Jager, van Keulen, and Kessels 2013)
Figure 1: The New European Driving Cycle (NEDC), the velocity profile used in this project's DP optimization. REFERENCE HERE
Figure 3: Battery model circuit.
1. Preface
  1. Reserach group description
2. Introduction
  1. Introduction to HEVs
  2. Energy Management Systems
  3. Project objectives for Summer Internship
    1. C port existing DP-PMP power management system
    2. Develop own DP algorithm optimizing fuel use
      1. Based on three state variables: discretized battery energy level, integer engine on-off control, and discrete gear state.
    3. Control theory – tie in to EE
3. Problem Description
  1. Vehicle Model
    1. Working with a priori New European Driving Cycle (NEDC) speed and slope profile data.
    2. Longitudinal vehicle dynamics model at wheel
    3. Powertrain model
    4. Power split optimization.
  2. Optimization Strategy Explanations
  3. Problem Formulation
4. Solutions to Problem Description
  1. Original Stephans DP-PMP model
    1. Port to C in order to lower computation demand for implementing management system into a rapid control protyping device.
  2. Dynamic Programming
    1. Finding optimal power split control of an HEV

Developing Optimal Power Split Controls in Hybrid-Electric Vehicles through
Dynamic Programming Optimization
Electronics Project Internship Report
Asgard Kaleb Marroquin
Technische Universität Dresden, Germany
Summer 2016

Acknowledgements
I would like to especially thank Stephan Uebel, Robert Kloss, Conny Tempelhahn, and Prof. Dr.-Ing. Bernard Baeker for the opportunity to work on such a fascinating subject this summer. Their mentoring, supervision, and advice was instrumental in understanding and developing optimal control theory this summer. I also thank all those at the Innovationzentrum Fahrzeugmechatronik, whose openness and inclusiveness helped me integrate into the mechatronics team professionally, academically, and culturally.
Preface
My internship this summer took place in Dresden, a small city on the east side of Germany, where industry and STEM-related technical training have taken strong root. In particular, I interned with the Innovationzentrum Fahrzeugmechatronik, or the Department of Vehicle Mechatronics, at the Technische Universität Dresden. The department works directly with the transportation agency in Dresden – the Dresdener Verkehrsbetriebe (DVB) – in reducing fuel consumption and heat losses in the city's ever-growing hybrid-electric bus fleet. The group also collaborates with private companies such as BMW, Daimler, Honda, Volkswagen, Continental, Evobus, and MAN. The department investigates various vehicle fields, such as power optimization strategies for powertrain management, thermal losses as a result of passenger exchange and a smaller combustion engine size, bus log data analysis, battery technologies, real-time component diagnostics, and conductor assistant systems for more efficient driving cycles.
Introduction
WRITE INTRODUCTION TO HEVS – necessary?
Various control methods have been investigated for optimizing energy management systems, or EMSs, for HEV powertrains. Two main control strategies exist for developing optimal HEV powersplit strategies: numerical methods for known a priori speed trajectories demand profiles (noncausal) and analytical methods without such knowledge (causal) (Jager, van Keulen, and Kessels et al 2013; Elbert 2013). Noncausal methods, requiring perfect future driving condition predictions, are able to compute across the entire given driving profile and find globally optimal solutions for EMSs (Tempelhahn 2016). Were noncausal optimization methods be used in realtime, stochastic inputs deviating from the defined driving cycle would influence calculations; as a result, such methods are typically performed offline and are used as benchmarks for comparing and designing efficient online causal EMSs (Tempelhahn 2016). Causal methods performing online, on the other hand, can only optimize locally portions of the driving cycle problem and thus return suboptimal strategies (Tempelhahn 2016).
Dynamic programming (DP) is typically used for calculating globally optimal EMS solutions due to its flexibility and ability to ensure global optimality. DP can utilize both mixed-integer and continuous state variables with nonlinear and nonconvex models, conditions which other methods cannot numerically make function (Elbert 2013; Murgovski et al 2013). However, dynamic programming can only practically optimize an EMS using a limited number of state variables because computational time increases exponentially as more state permutations for a given driving profile are analyzed – i.e. the “curse of dimensionality” (R. Bellman, Dynamic Programming, Princeton, NJ. USA: Princeton Univ. Press, Jun. 1957). DP also requires predetermined travel profile data and is thus noncausal by nature. Nevertheless, due to the repetitive, predictable nature of city bus routes, speed profiles for hybrid-electric transit can be approximated based on past logged data records. Standard driving trajectories, such as the New European Driving Cycle, attempt to mimic urban driving speed profiles and are typically used for determining typical urban emissions (INSERT REFERENCE); these trajectories can also be used as a baseline for testing HEV EMSs.
Alternative causal optimization methods such as convex optimization and methods utilizing Pontryagin's maximum principle (PMP) are also researched in order to implement online control systems in HEVs. Although far faster than DP, such methods naturally have their limitations. For example, convex optimization requires a linear convex model utilizing continuous state variables in order to function effectively. Should a problem be originally nonconvex, it must be manually made convex, possibly affecting optimality results (Tempelhahn, Conny 2016). And although mixed-integer boolean state variables – engine on-off control, for example – can be theoretically relaxed to become a continuous value between zero and one (Murgovski, Nikolce et al 2013), it was agreed upon by the research group that smoothing out strict boolean controls may yield questionable results at best and the proceudure may not yet be generally accepted as sound. PMP-based strategies are also limited to processing only continuous state variables, but can also find near-globally optimal results for such variables (Tempelhahn, Conny 2016).
Due to the strengths and weaknesses of various different optimization control methods, they are usually combined and synergize with each other's characteristics. Faster procedures such as convex optimization and PMP can be integrated into DP algorithms and optimize the continuous variables in the model. This frees up the number of states DP must calculate and dedicates the algorithm to optimize just mixed-integer states, considerably reducing computation time as a result (Uebel, Stefan et al 2016, Murgovski, Nikolce et al 2013). Should an accurate DP-PMP combined method become fast enough on either a predictable hybrid-electric bus route profile or a model European driving cycle,

Two main projects were defined for this summer internship. The first involves further speeding up and converting a MATLAB DP-PMP algorithm developed by my supervisor into C/MEX so that it may be tested in a Autobox, a rapid control prototyping device. This algorithm uses vehicle kinetic energy, battery electric energy, gear selection, and travel time as state variables to minimize fuel use for an articulated bus model, making control decisions at a spatial resolution of every ten meters. The details of this control methods can be found in (Uebel, Stefan et al 2016). This project aided in learning the fundamentals of dynamic programming and modern controls through “hands-on” experience with DP, and proved invaluable for completing the second project described in this report. more relevant to working with control, involved developing a new DP algorithm which would find the optimal power split control of a Ford Focus-like HEV model based on battery energy levels, discrete gears, and boolean engine on-off states. The temporally resolved offline model, requiring a predefined driving profile, is based on the New European Driving Cycle. By creating a dynamic programming model based on modern control theory which models and optimizes battery use in a hybrid-electric bus at a macroscopic level, this internship has taught me the principles of controls, a fundamental field of electrical engineering.
In order to describe the project in detail, the vehicle model utilized this summer is first described. The state variables – battery energy, gear, and engine state – for the model and state dynamics controlling changes in the state variables are also defined. The two sections are afterwards into a description of the DP model minimizing the given cost function – that is, fuel use. Results from the algorithm showing optimal trajectories for various possible final ending battery energy states are shown and discussed.
DESCRIBE DYNAMIC SYSTEM
Problem Description
New European Driving Cycle
The New European Driving Cycle (NEDC), a speed profile mimicking a typical commute in a European urban environment, is used as a vehicular travel profile for the DP algorithm (Figure 1). The driving cycle consists of four Urban Driving Cycle (UDC) periods of driving simulating sporadic low vehicle speed and engine load experienced in cities, followed by an Extra Urban Driving Cycle (EUDC) simulating faster, more aggressive travel (United Nations Environment Programme).
State Variables
The HEV is being optimized for minimal fuel use based on three state variables: battery buffer state of charge (SOC) energy level EB, gear selection g, and engine on-off decision e (-2).
bold x = langle E_B, g, e rangle (-2)
Control signals for the discrete gear and engine states are also defined as an input vector (-1).
bold u = langle u_g, u_e rangle (-1)
The battery energy level EB, a continuous variable in reality, must be discretized so that the state variable can exist in the DP state space. The finer the resolution, less overshoot will occur and the algorithm would yield more accurate results. However, more finely resolved changes in EB require exponentially more computing time, due to the increased number of possible EB states and thus must check additional state variable permutations. Therefore, a resolution of 2500 J is chosen in order to attempt to balance these two factors.

Vehicle Model
In order to optimize the power split control in the HEV, a vehicle model able to satisfy the wheel torque demand satisfying the NEDC must be defined. Vehicle model parameters, (eg vehicle mass, battery power and energy limits, internal combustion engine (ICE) and electric motor (EM) speed and torque bounds, etc), in this model are based from a hypothetical Ford Focus HEV.
Defining the power demand split for an HEV will depend on the vehicle's drivetrain architecture. The model works with a parallel drivetrain, in which the ICE and the EM are completely decoupled. This permits both machines to independently contribute to the requested crankshaft power demand PCRS (Jager, van Keulen, and Kessels 2013).As engine on-off control e is a state being optimized for in this EMS, the ICE can either contribute power PICE to (e=1) or be disengaged from (e=0) the crankshaft, leaving the EM to supply enough power PEM to completely satisfy PCRS for the given time index decision moment (0). Should a given PICE exceed the PCRS demand, the excess power can go back into recharging the battery buffer (Figure 2).
bold P_ICE(bold x) = left lbrace binom{bold P_CRS(g) - bold P_EM(E_B) if e = 1} {0 if e = 0} right none (0)
To calculate the requested power demand, the crankshaft speed and the sum of forces at the wheel must first be determined. The vehicle's velocity vector v, wheel constant rolling radius r, and gear ratio γ(g) define the crankshaft's rotational velocity ωCRS(g) (1), where v is the NEDC speed profile discretized every second.
bold %omega_CRS(g) = bold v over r%gamma(g) (1)
The forces at the wheel can be described though use of Newton's Second Law (2),
INCLUDE TIME
m {d bold v } over {dt} + bold c_%alpha + bold c_%beta + c_a bold v^2 + F_B = (bold F_WHEEL)%gamma(g) (2)
where m is the vehicle mass, dv/dt is vehicular acceleration, cα = m*g*sin(Θgradient) is the vehicle's gradient force, cβ = μdrag*m*g*cos(Θgradient) is the vehicle drag force, Θgradient is the speed trajectory's slope profile (defined here flat). FB are braking forces, and FWHEEL is the amount of force the wheel must deliver.
The wheel torque demand TWHEEL = FWHEEL*r for the NEDC is found and subsequently the crankshaft torque TCRS (3) and power PCRS (3a) are derived. The powertrain split satisfying PCRS between the internal combustion engine's torque PICE and electric motor's torque PEM is what is optimized for this HEV's EMS during DP calculations.
bold T_CRS(g) = left lbrace binom{bold T_WHEEL over {%gamma(g)} * %eta_g for bold T_CRS( bold T_WHEEL < 0)} {bold T_WHEEL over {%gamma(g)} / %eta_g for bold T_CRS( bold T_WHEEL >= 0)} right none (3)
bold P_CRS(g) = bold T_CRS(g) * bold %omega (g) (3a)
Battery Model
Describing the effects of EB's state dynamics (4) on the crankshaft power demand requires a battery model illustrating the intermediate processes (Figure 3).
E'_B = f(E_B) = P_B * %DELTA t (4)
Rearranging (4), using a select possible present and predecessor EB value yields a battery power PB(t) for the given time index (5).
P_B(t) = {E_B(t) - E_B(t-1)} over {%DELTA t} (5)
In this model, dissipation conversion losses PEM, loss, input auxiliary power PAUX, and internal battery losses PB,loss are taken into consideration when translating a change in the state EB into PEM (6).

P_EM(t) - P_EM,_loss = P_EM,_electric(t) = P_B(t) - P_B,_loss - P_AUX (6)
Electric battery power losses can be easily derived from Ohm's Law. The amount of electric power transferred to the EM is simply the difference between the battery's terminal power (7) and the battery's internal losses (8)..
P_B = V(E_B)I (7)
P_B,_loss=I^2 R( E_B ) (8)
If a certain EB level is being evaluated, as is the case when looping through various EB values in DP, the battery current I can be easily calculated from (7), allowing for a straightforward PB,loss calculation in (8). Otherwise, if a sample PEM,electric is given instead (for example, during preprocessing when setting bounds on reachable EB states), equation (6) must be rearranged so that the battery current I can be calculated quadratically and substituted back into (8), as shown in (9).
P_B,_loss = {V(E_B) - sqrt(V^2 (E_B) - 4R P_EM,_electric )} over {4R} (9)
The battery's open circuit voltage V is nonlinearly dependent on EB. V is derived from a model input lookup table. INCLUDE GRAPH OF OCV WRT SOC? The internal resistance R will have a different sign (and possibly a different value) if either the input PB or PEM, electric (depending on how I was calculated, during DP or preprocessing, respectively) is charging or discharging the battery (10).
R = left lbrace binom{R_CHARGE for (P_B > 0 or P_EM,_electric > 0) } {R_DISCHARGE for (P_B <= 0 or P_EM,_electric <= 0)} right none (10)
State Variable Bounds
Bounds must also be placed on the state variables due to physical limitations. Because the entire speed demand profile is known ahead of time, various bounds for EB can be calculated beforehand. Two bounds for EB's state dynamics (PB,MIN and PB,MAX) are preprocessed: power limitations based on the HEV model's EM speed limits PEM, MIN(ωCRS,, t) and PEM, MAX(ωCRS, t), and power limitations based on the model battery's energy charge/discharge limits PBAT. Gear changes ug are also bounded so that the gear can only transition to adjacent states from one time interval to the next.
It should be noted that at the time of this report that I am analyzing whether PEM, MIN(·) and PEM, MAX(·) referred to mechanical or electrical power limitations. I originally treated it as an electrical power limitation based on rotational velocity limitations of the EM. Should however these parameters refer to physical limits instead, an additional power conversion term during preprocessing must be added to account for losses. I plan to address this issue with my mentor in the very near future in order to ensure optimal results. This issue occurs only when working with an input PEM, electric when preprocessing, and not when running through EB states when running DP (that is, when working through equation (6) left to right instead of right to left). Physical EM torque TEM can be interpolated from a lookup table based on ωCRS and PB (derived from g and EB states, respectively); because the the nonlinear conversion loss is included TEM interpolation, the physical EM power PEM(EB, g) = TEM(EB)*ω(g) can be derived when EB is provided.
This preprocessing drastically reducing computational time while running DP, as various physically unreachable states were immediately ignored during calculations. In this DP algorithm, calculation time dropped drastically after implementing preprocessed bounds from 24 hours to just over fifteen minutes. Defining these bounds beforehand for all possible crankshaft speeds and torques through time removes the rote calculation otherwise required in DP when bounds would have to be calculated for each time interval and nested previous and current state permutation loops.

Objective Function
The objective of this EMS is to, given set of initial and ending state variable conditions, find the path burning the least amount of fuel for the NEDC trajectory. The objective function (11) is the integral of the ICE's power along the path with respect to time, along with any penalties defined for switching gear (βg) or engine (βe) states. Because this function must analyze both the current change in EFUEL as well as the cumulative effect of all previously selected EFUEL values, each change in EFUEL at time index t all previous reachable states x(t-1) (with their respective control signals u(t-1) and state dynamic f(EB(t-1)) must be calculated for every given state x(t). Thus, in order to calculate the minimum value, recursive effects of predecessor states x for every given selected EFUEL must be taken into consideration; otherwise, the algorithm is greedy and will not ensure a global optimum ().
minimize E_FUEL = int from{t_i} to{t_f} {((P_ICE(bold x, bold u) + P_ICE,_loss) + lline u_g rline %beta_g+ lline u_e rline%beta_e)dt} = int from{t_i} to{t_f} %LAMBDA (bold x, bold u )dt (11)
Dynamic Programming Implementation
Now that the state variables, battery dynamics, gear and engine control signals, vehicle and battery models, and a objective cost function to minimize for have been defined, dynamic programming can be used to run through each realistic state variable permutation through the use of nested for-loops. DP is based on Bellman's Principle of Optimality, where, for a given problem which can be broken up into smaller subproblems, the globally optimum path in the problem be comprised of smaller optimal paths along its intermediate steps (R. Bellman, Dynamic Programming, Princeton, NJ. USA: Princeton Univ. Press, Jun. 1957). Therefore, given initial and final state conditions, DP can be run forwards or backwards in time and calculate the optimal trajectory either way. In this model, DP is run forwards in time with intermediate steps spaced one second apart in time

minimize %LAMBDA_t,_f (bold x) + sum from{k=t_i} to{t_f-1} {%LAMBDA_k (bold x, bold u )%DELTA t} (12)
f(E_B) in {[P_B,_MIN , P_B,_MAX]} (12a)
g( t+1 ) = g(t) + u_g (12b)
e(t+1 ) = u_e (12c)
bold x(t_i) = bold x_i, bold x(t_f) = bold x_f (12d)
bold x in {[bold x_min, bold x_max]} (12e)
u_g = lbrace -1, 0, 1 rbrace (12f)
u_e = lbrace 0, 1 rbrace (12g)

References
Elbert (2013)
United Nations Environment Programme